## Slide 1: Air Traffic Services
Civil Aviation University of China
Civil Aviation University of China

## Slide 2: Learning objectives
Objectives:
  State the objectives of ATS
  List the types of separation
  Explain wake turbulence
  Describe the criteria for the use of runway
  State the five legs of an aerodrome traffic pattern
  Describe the functions of an approach controller
  State the objectives of Flight Information Service
  State the objective of Alerting Service
  State the three phases for alerting service
References:
  ICAO Annex 11
  ICAO Doc 9426
  ICAO Doc 4444

## Slide 3: Objectives of the air traffic services
  prevent collisions between aircraft;
  prevent collisions between aircraft on the maneuvering area and obstructions on that area;
  expedite and maintain an orderly flow of air traffic;
  provide advice and information useful for the safe and efficient conduct of flights;
  notify appropriate organizations regarding aircraft in need of search and rescue aid, and assist such organizations as required.
ATC
FIS
Alerting Service

## Slide 4: Air Traffic Control Service
Tools
  Radar
  VHF
Information
  Traffic information
  Environment information
    Terrain
    Weather
Output
  Clearances, instructions, information
Objectives
  Safety & efficiency

## Slide 5: Controller Information Processing
Situation Awareness
Perception
of elements
in current
situation
Level 1
Comprehension of Current situation
Level 2
Projection of future status
Level 2
Decision
Action
Information Processing
Mechanisms
Long-term
Memory stores
Automaticity
Abilities
Experience
Training
Goals & Objectives
Expectations
System capability
Interface design
Stress & workload
Complexity
Automation
State of
The traffic
situation
Feedback

## Slide 6: Types of Separation
VFR separation
IFR separation (non-radar)
Radar separation
Wake turbulence separation
Vertical separation
Lateral separation
Horizontal separation
Composite separation
Time separation
Distance separation

## Slide 7: Visual Separation
For VFR flights in uncontrolled airspace
For IFR flights under certain condition
See and avoid

## Slide 8: IFR separation (non-radar)
10min
Two aircraft flying on the same track, at the same level and speed:
10 minutes/5 min/3 min

## Slide 9: IFR separation (non-radar)
6600m
6300m
6000m
15min
15min
15min
For an aircraft changing level through the level of another on the same track, a minimum longitudinal separation of 15 min/5min

## Slide 10: IFR separation (non-radar)
6600m
6300m
6000m
Estimated Point of passing
10min
10min
For an aircraft changing level to cross the level of another in reciprocal flight, the former may climb to a level above, or descend to a level below the latter 10 minutes prior to the estimated point of passing

## Slide 11: IFR separation (non-radar)
one aircraft may cross the level of another 10 minutes after the estimated point of passing
6600m
6300m
6000m
10min
10min
Estimated Point of passing

## Slide 12: IFR separation (non-radar)
15 min
For two aircraft on crossing tracks at the same level, a longitudinal separation of 15 min/10 min

## Slide 13: IFR separation (non-radar)
50 km
VOR
15º
VOR separation

## Slide 14: IFR separation (non-radar)
50 km
NDB
30º
NDB separation

## Slide 15: IFR separation (non-radar)
DME separation
DME
40 km
20 km
DME
20 km

## Slide 16: IFR separation (non-radar)
6600m
6300m
6000m
20 km
20 km
20 km
DME
DME separation

## Slide 17: Radar Separation
ACC 10 km
APP 6 km
6 km
Where radar control is implemented, radar separation minima shall be :
(1) 6 kilometers in approach control domain, and
(2) 10 kilometers in area control domain

## Slide 18: Wake turbulence Separation
Wake turbulence separation shall be applied to avert the effect of wake turbulence

## Slide 19: Wake turbulence Separation
Wake turbulence separation shall be applied between departing and departing, and arriving and arriving.
Wake turbulence separation minima is determined by maximum certificated takeoff mass.
Aircraft are classified according to their maximum certificated takeoff mass into three categories.
HEAVY:  136,000 kg
136,000 kg > MEDIUM > 7,000 kg
LIGHT:  7,000 kg

## Slide 20: Wake turbulence Separation
Wake Turbulence Separation Based on Distance |  | 
Leading Aircraft | Following Aircraft | Separation Minima (km)
HEAVY | HEAVY | 8
HEAVY | MEDIUM | 10
HEAVY | LIGHT | 12
MEDIUM | LIGHT | 10
MEDIUM | HEAVY | 6
Airbus 380 |  | X + 4

## Slide 21: Wake turbulence Separation
Wake Turbulence Separation Based on Time |  | 
Leading Aircraft | Following Aircraft | Separation Minima (min)
HEAVY | HEAVY | 2
HEAVY | MEDIUM | 2
HEAVY | LIGHT | 3
MEDIUM | LIGHT | 3

## Slide 22: Wake turbulence Separation
The deficiency with existing Wake Turbulence Separation Minima?
How to design a dynamic WTSM system?
  Better categorization
  Atmospheric condition detection
  Wake turbulence detection
  Friendly presentation to the controller

## Slide 23: Aerodrome Control
Aircraft taxiing on the taxiways
Use of the runway
Aircraft in the vicinity of the aerodrome

## Slide 24: Use of the runway
A departing aircraft will not normally be permitted to commence take-off until the preceding departing aircraft has crossed the end of the runway-in-use or has started a turn or until all preceding landing aircraft are clear of the runway-in-use.

## Slide 25: Use of the runway
A landing aircraft will not normally be permitted to cross the runway threshold on its final approach until the preceding departing aircraft has crossed the end of the runway-in-use, or has started a turn, or until all preceding landing aircraft are clear of the runway-in-use.

## Slide 26: Aerodrome Traffic Circuit
Under VMC, Aircraft may follow a traffic circuit and make a landing

## Slide 27: Aerodrome Traffic Circuit
Downwind
Final
Base
Crosswind
Upwind
Wind

## Slide 28: Aerodrome Control

## Slide 29: Approach Control
Metering
Merging
Sequencing
Spacing

## Slide 30: Approach Control

## Slide 31: Area Control

## Slide 32: Flight Information Service
SIGMET and AIRMET information;
information concerning pre-eruption volcanic activity, volcanic eruptions and volcanic ash clouds;
information concerning the release into the atmosphere of radioactive materials or toxic chemicals;
information on changes in the serviceability of navigation aids;
information on changes in condition of aerodromes and associated facilities, including information on the state of the aerodrome movement areas when they are affected by snow, ice or significant depth of water;
information on unmanned free balloons;
weather conditions reported or forecast at departure, destination and alternate aerodromes;
collision hazards, to aircraft operating in airspace Classes C, D, E, F and G;
for flight over water areas, in so far as practicable and when requested by a pilot, any available information such as radio call sign, position, true track, speed, etc., of surface vessels in the area.

## Slide 33: Flight Information Broadcasts
OFIS- Operational Flight Information Service
ATIS – Automatic Terminal Information Service
VOLMET – Meteorological information for aircraft in flight

## Slide 34: Alerting Service
Three phases
  Uncertainty phase
  Alert phase
  Distress phase

## Slide 35: Alerting Service
Uncertainty phase when:
  no communication has been received from an aircraft within a period of 30 minutes after the time a communication should have been received, or from the time an unsuccessful attempt to establish communication with such aircraft was first made, whichever is the earlier, or when
  an aircraft fails to arrive within 30 minutes of the estimated time of arrival last notified to or estimated by air traffic services units, whichever is the later,

## Slide 36: Alerting Service
Alert phase when:
  following the uncertainty phase, subsequent attempts to establish communication with the aircraft or inquiries to other relevant sources have failed to reveal any news of the aircraft, or when
  an aircraft has been cleared to land and fails to land within 5 minutes of the estimated time of landing and communication has not been re-established with the aircraft, or when
  information has been received which indicates that the operating efficiency of the aircraft has been impaired, but not to the extent that a forced landing is likely, except when evidence exists that would allay apprehension as to the safety of the aircraft and its occupants, or when
  an aircraft is known or believed to be the subject of unlawful interference.

## Slide 37: Alerting Service
Distress phase when:
  following the alert phase, further unsuccessful attempts to establish communication with the aircraft and more widespread unsuccessful inquiries point to the probability that the aircraft is in distress, or when
  the fuel on board is considered to be exhausted, or to be insufficient to enable the aircraft to reach safety, or when
  information is received which indicates that the operating efficiency of the aircraft has been impaired to the extent that a forced landing is likely, or when
  information is received or it is reasonably certain that the aircraft is about to make or has made a forced landing.

## Slide 38: Questions
  What are the objectives of ATS
  What are the types of separation
  What is the determining factor on wake turbulence?
  Under what circumstances can an arriving aircraft be permitted to land?
  Under what circumstances can a departing aircraft be permitted to take off?
  What the five legs of an aerodrome traffic pattern
  What are the main functions of an approach controller?
  What is the objective of Flight Information Service?
  What is the objective of Alerting Service?
  What are the three phases for alerting service?