## Slide 1: Questions
What airspace structures does FUA use?
What are the three levels of flexible management of airspace?
What are the functions of an Airspace Management Cell?
What are the differences of Flexible Use of Airspace and Dynamic Airspace Management?

## Slide 2: FUA Concept
Airspace should no longer be designated as either military or civil airspace but should be considered as one continuum and used flexibly on a day-to-day basis.
Consequently, any necessary airspace segregation should be only of a temporary nature.
The daily allocation of flexible airspace structures, that any necessary segregation of airspace is based on real usage within a specific time period.
FUA Concept uses airspace structures that are particularly suited for temporary allocation and/or utilization.
The different airspace structures includes:
  Conditional Routes (CDRs),
  Temporary Reserved Areas (TRAs),
  Temporary Segregated areas (TSAs), or
  Cross-Border Areas (CBAs) and
  Prior Co-ordination Airspace (PCA) or
  Reduced Co-ordination Airspace (RCA) procedures.
Notes: FUA：Flexible Use of Airspace.
1.空域不应再根据军用和民用划分，应统一起来，一起使用
2.逐渐的，任意空域性质划分应只是暂时性的
3.空域灵活划分应基于特定时间段内的实际应用
4.FUA使用的空域结构应该符合暂时性分配和使用
5.不同空域结构包括：有条件的航路，临时性保留区，临时性分配区，跨界区，优先协调空域，减少协调空域程序

## Slide 3: Levels of ASM
  Tactical ASM - Level 3.
The FUA Concept is based on 3 Levels of ASM as:
  Pre-Tactical ASM - Level 2
  Strategic ASM - Level 1,

## Slide 4: Strategic ASM
Strategic ASM at Level 1 consists of a joint civil and military process within a high-level civil/military national body, which formulates the national ASM policy and carries out the necessary strategic planning work, taking into account national and international airspace users requirements.
In order to maintain a flexible airspace organization, States assess and re-assess their national airspace and routes structures. At Level 1, the States determine the working structures for ASM Levels 2 and 3, and give them the agreed minimum authority to carry out their tasks. The States lay down the procedures to be followed at these tactical and pre-tactical levels and agree priority rules and negotiation procedures for airspace allocation at Level 2 and Level 3.
To enable a continual improvement of the efficiency of airspace use, the States will conduct a periodic review of national airspace and route structures. This periodic review will include the detailed analysis of ASM planning and operations at Levels 1, 2 and 3.

## Slide 5: Pre-Tactical ASM
Pre-Tactical ASM at Level 2 consists of the day-to-day management and temporary allocation of airspace through national or sub-regional AMCs.
AMCs are joint civil/military ASM focal-points which have the authority to conduct operational ASM within the framework of the States airspace structures, priority rules and negotiation procedures as laid down by the national policy body. AMCs collect and analyze all airspace requests and decide the daily airspace allocation. AMCs promulgate the airspace allocation as an Airspace Use Plan (AUP) and amendments thereto through Updated Airspace Use Plans (UUPs).
In Europe, an ECAC Centralized Airspace Data Function (CADF) is established within the CFMU. The CADF collects availability information on non-permanent ATS Routes called Conditional Routes (CDR) from the various AUPs and compiles it into a consolidated list called the Conditional Route Availability Message (CRAM) and, when necessary, a CRAM Correction Message The CRAM and CRAM Correction Messages are used by Aircraft Operators (Aos) for flight planning purposes.

## Slide 6: Tactical ASM
Tactical ASM Level 3 consists of the real-time activation, deactivation or real-time reallocation of the airspace allocated at Level 2 and the resolution of specific airspace problems and/or traffic situations between civil and military ATS units and/or controllers, as appropriate.
Flexibility in the use of airspace is enhanced by real-time civil/military co-ordination capability. This flexibility depends on the potential offered by the joint use of airspace by civil and military traffic.
Real-time access to all necessary flight data, including controller’s intentions, with or without system support, permits the optimized use of airspace and reduces the need to segregate airspace.

## Slide 7: Operation of Airspace Management Cell
AMC
Flexible Airspace Tools
TSAs
CBAs
CDRs
National/
International Guidelines
Authority
Priority Rules
Negotiation Procedures
Protocols
International Agreements
Area
Control
Centers
Flow Management Positions
Approved Agencies
Other
AMCs
Area Control
Centers
Flow Management Positions
Central Airspace Data Functions
Approved Agencies
Other
AMCs
TEMPORARY AIRSPACE REQUESTS
AIRSPACE USE PLAN (AUP/UUP)

## Slide 8: Enhanced Basic FUA Process with Dynamic Airspace Management
ASM |  | Level 1 | Level 2 | Level 3
Airspace Delineation | Basic FUA | Airspace Design Process Establishment of airspace structures (with a limited number of scenarios) |  | 
 | Dynamic Airspace Management | Establishment of airspace structures offering greater choice of route options and flexibility to extend/sub-divide military training areas Ad-hoc Airspace Delineation Process | Ad-hoc structure | Ad-hoc structure
Airspace Allocation | Basic FUA | Priority Rules and Negotiation Process | Current AMC Process | Limited to real-time activation/deactivation
 | Dynamic Airspace Management | “Modus Operandi” of pre-defined scenarios | Enhanced AMC process moved closer to time of operation | Collaborative decision-making process at short notice
Information Dissemination | Basic FUA | AIP NOTAM | AUP/UUP/CRAM | Tel/Fax/radio/NOTAM/Data Processing
 | Dynamic Airspace Management | Airspace Data Repository | Airspace Data Repository | Airspace Data Repository Tel/Fax/radio/NOTAM/
Notes: modus operandi 做法, 惯技

## Slide 9: Dynamic Airspace Management
The intent of Dynamic Airspace Management is to establish a process exploiting the airspace in a dynamic manner by enabling late airspace allocation/re-allocation, where required as close as practical to the time of operations to accommodate short-term changes in traffic situation and/or users requirements.