## Slide 1: Air Traffic Flow & Capacity Management
Civil Aviation University of China
Civil Aviation University of China

## Slide 2: Learning Objectives
Objectives:
  State the objectives of ATFM
  Describe the main causes of air traffic congestion
  Describe the functions of ATFM
  Describe the three phases of ATFM
  Define the concept of capacity
  List the ways to maximize en route capacity
  List the methods for the assessment of airspace capacity
  List the methods for the assessment of airport capacity
References:
  Air Traffic Flow & Capacity Management Strategy
  Air traffic Flow and Capacity Management Evolution Plan for the ECAC States

## Slide 3: Major World Air Traffic Flows

## Slide 4: Major Traffic Flows in China

## Slide 5: The objective of air traffic flow & Capacity management
To ensure an optimum flow of air traffic to or through areas during times when demand exceeds, or is expected to exceed, available capacity of the air traffic control (ATC) system.

## Slide 6: Flight Delays in China

## Slide 7: The main causes of the air traffic congestion
accumulation of air traffic during specific periods of the year and also during certain times of the week and hours of the day, due to holiday patterns and travel habits of the public;
differences in the capacities of the various ATC systems or parts of these systems affected by traffic accumulations;
insufficient advance notice (to ATC units) of likely traffic demands which may cause overloading of the system at certain points, in certain areas, and/or during specific time periods;
lack of proven techniques and procedures to restore, in critical situations, a reasonable balance between traffic demand and available ATC capacity by means acceptable to aircraft operators both from an operational and from an economic point of view.

## Slide 8: The Consequences of Air Traffic Congestion
An optimum flow of air traffic is not always possible due to various constraining factors, such as conflicting users’ requirements, air navigation system limitations and unexpected weather conditions.
In this connexion, alleviating measures, such as control of air traffic flow, will need to be considered, particularly when the ATC system can no longer fully cope with the volume of air traffic.
Such measures frequently result in delays of flights prior to departure, in-flight holdings, use of uneconomic flight levels, re-routing and diversions, disruptions of flight schedule, economic and fuel penalties for aircraft operators, congestion on aerodromes or in terminal buildings and passenger dissatisfaction.

## Slide 9: The functions of ATFCM
collection and collation of data on the air navigation infrastructure and on the capacities of the ATC system and selected aerodromes within the area, including runway, taxiway and gates capacities. This embraces those areas in which traffic flow problems are likely to be encountered;
collection and analysis of data for all planned controlled flight operations into, out of, within and through the area;
determination of a coherent picture of expected traffic demand, including anticipated ad hoc traffic, comparison with available capacity and identification of areas and time periods of expected critical traffic loadings;
co-ordination with the appropriate ATS authorities in order to make every possible attempt to increase the available ATC capacity where required. In some particular situations it could be advantageous for national and local scheduling committees to be established, with representatives from national ATS, airport authorities, national and international operators. Such committees can make significant contributions when developing strategies to reduce the impact of peak demand periods; and where ATC capacity shortfalls cannot be eliminated, determination and implementation in good time of suitable tactical measures coordinated throughout the area as necessary and with aircraft/aerodrome operators concerned.

## Slide 10: The functions of ATFCM
Overload !
Capacity
Time
Initial Demand
Capacity
Time
Regulated Demand

## Slide 11: Flow management procedures
Strategic Planning
Pre-tactical Planning
Tactical operation
The Day of Operation
The Previous Day
2~6 months ahead

## Slide 12: Strategic planning
Strategic planning is be carried out in conjunction with ATC and the aircraft operators. It should consist of examining the demand for the forthcoming season, assessing where and when demand is likely to exceed the available ATC capacity and taking steps to resolve the imbalance by:
  arranging with the ATC authority to provide adequate capacity at the required place and time;
  re-routing certain traffic flows (traffic orientation);
  scheduling or rescheduling flights as appropriate; and
  identifying the need for tactical ATFM measures.

## Slide 13: Pre-tactical planning
Pre-tactical planning should entail fine-tuning of the strategic plan in the light of updated demand data. During this phase:
  certain traffic flows may be re-routed;
  off-load routes may be coordinated;
  tactical measures will be decided upon; and
  details for the ATFM plan for the following day should be published and made available to all concerned.

## Slide 14: Tactical operations
Tactical ATFM operations should consist of:
  executing the agreed tactical measures in order to provide a reduced and even flow of traffic where demand would otherwise have exceeded capacity;
  monitoring the evolution of the air traffic situation to ensure that the ATFM measures applied are having the desired effect and to take or initiate remedial action when long delays are reported, including re-routing of traffic and flight level allocation, in order to utilize the available ATC capacity to the maximum extent.

## Slide 15: Possible ATFCM Solutions for Capacity Shortfalls Resolution
CAPACITY | SHORTFALLS | OPTIMISE UTILISATION OF AVAILABLE CAPACITY
 | UTILISE OTHER AVILABLE CAPACITY | Sector Management Configuration Number of sectors Civil/Military Co-ordination Reduce Traffic Complexity Review Capacity Value Holding Pattern Balancing Arrival/Departure Capacity
REGULATE THE DEMAND | Re-routing Flows Flight FL Management Advancing Traffic | 
Restrictions Acting on Airborne Traffic |  | 

## Slide 16: The three phases of ATFCM
1 year
1 week
Real-time
Traffic Forecast
Resources
Airspace
ATC
Airport
Strategic Flow & Capacity Planning
Establishment of scenarios and harmonized planning considering:
Traffic Demand
Airspace Structure
ATC Capabilities
Airport Capabilities
Optimized Capacity Management
Pro-active optimization of the Network Operations Plan and anticipation of events in order to maintain the network stability
Tactical Flow&
Capacity Management
Monitoring of the ATFCM situation and reaction to real-time events to minimize disruption impact and/or to take benefit of opportunities
Real-Time Operations
ATC
ASM
Airport
AOs
Feedback
Feedback
Feedback
Feedback
Planning
Execution

## Slide 17: Working Process for Strategic ATFCM
Reduction of Traffic Demand in critical areas
ASM
Airspace Structure
(routes, sectors, etc) including capacity values
ATC
Capabilities
(Staff resources, operating techniques, system support)
Airport
Capabilities
(Schedule, infrastructure, etc)
ATM Environment
AO Traffic Forecast
Are
There Capacity shortfalls?
Are
There Capacity shortfalls?
Acceptable but requiring Pre-tactical and/or Tactical fine-tuning
Define Scenarios/Modus Operandi (routes, areas, sectors)
Pre-validation of scenarios and airspace structure before any publication (AIP, RAD, etc)
Provision of data required to conduct Pre-tactical Activities
(e.g. RAD. Environment Database, Daily Capacity Plans, etc)
Pre-tactical & Tactical Working Processes
Maximize Network Capacity
Airport Capacity
En-route Capacity
Holding Patterns
Arr/Dep
Capacity
Reduce Traffic Complexity
Increase Capacity Value
Adapt the Sector Configuration
Adapt the Number of Sectors
Civil/Military Coordination
Consider the following elements
Identify the sectors/airports concerned
Other capacity
FL management
Re-routing Flows/Flights
Request for Changes & Feedback
NO
YES
Feedback
NO
YES
YES
CDM
ASM/ATSPs/Airport/AOs/FMD

## Slide 18
Are
there capacity shortfalls?
Identify the sectors/airports concerned
Adapt the sector configuration
Adapt the number of sectors
Civil/Military Coordination
Reduce traffic complexity
Increase Capacity value
Maximize En-route Capacity
Maximize airport Capacity
Holding Pattern
Arr/Dep
capacity
Are
there capacity shortfalls?
Is
Additional capacity?
Utilize other available capacity
Re-routing flows/flights
FL
Management
Advancing traffic
Are
there capacity shortfalls?
Could capacity be maximized?
Regulate the demand
Apply restrictions
Could capacity be maximized?
Network Operations Plan/Updates
Compare traffic demand with strategic ATFCM data
Organization of
ATC behavior
Influence on AOs behavior
Tactical Working Process
Strategic Working Process
Feedback
No
No
No
No
No
No
Yes
Yes
Yes
Yes
Yes
Yes
CDM
FMD/FMPs
FMD/ FMPs/ AMCs
FMD/FMPs
FMD/ FMPs/AMCs
Working Process for Pre-tactical ATFCM

## Slide 19
Consider real-time events according to the Network Operations Plan
Identify the sectors/airports concerned
Provision of a consolidated Network Flow & Capacity Picture for real-time operations
Rea-time Operations (ASM, ATC, Airport, AOs)
Are
there capacity shortfalls or opportunities?
Implement adequate real-time ATFCM solutions
Adapt the sector configuration
Adapt the number of sectors
Civil/Military Coordination
Reduce traffic complexity
Increase Capacity value
Maximize En-route Capacity
Maximize airport Capacity
Holding Pattern
Arr/Dep
capacity
Organization of ATC behavior
Utilize other available capacity
Re-routing flows/flights
FL
Management
Advancing traffic
Influence on AOs behavior
Regulate the demand
Apply restrictions
Constraining airborne traffic
Strategic Working Process
No ATFCM action required
Feedback
FMD/FMPs/ATC/ AOs/
AMCs
CDM
Working Process for Tactical ATFCM
No
Yes

## Slide 22: CFMU NETWORK
CFMU
FMP
FMP
FMP
AIRPORT
AIRPORT
AIRPORT
NETWORK
SMALL-SCALE NETWORK

## Slide 23: Airport Capacity Assessment
airport capacity is the maximum number of airport operations in a given aerodrome under specified conditions (e.g., aerodrome layout, aircraft mix, weather conditions, facilities, aircraft parking, etc.),
taking into account all
take-off and landing
operations during a
specified period of time
(hour, day, month,
year, season).

## Slide 24: Factors Impacting Airport Capacity

## Slide 25: Methodologies to Assess Airport Capacity
Analytic models
  Time-space analysis
  Queuing models (deterministic and stochastic)
Simulation-based models
  Monte Carlo Simulation
  Continuous simulation models
  Discrete-event simulation models

## Slide 26: Factors Impacting Airspace Capacity

## Slide 27: Methodologies to Assess Sector Capacity
Sector capacity is restricted by the controller workload
Methods:
  “DORATASK” method
  MBB Method
The essence of both methods was to measure the necessary time for all control working actions and to relate this time to the total time available.
The average workload at capacity must be less than 80% and workloads of 90% must not be exceeded more than 2.5% of the time

## Slide 28: Controller Task load
Observable tasks
  radiotelephony (RTF) and telephone communication,
  strip marking
  direct-voice-liaison coordination.
  Inputs, etc.
Non-observable tasks
  Monitoring the radar screen
  Planning future actions
Recuperation
Notes: Recuperation: To return to health or strength; recover.

## Slide 29: Questions
What are the objectives of ATFM?
What are the main causes of air traffic congestion ?
What are the functions of ATFM ?
What are the three phases of ATFM ?
What is the concept of capacity ?
What are the ways to maximize en route capacity ?
What are the methods for the assessment of airspace capacity ?
What are the methods for the assessment of airport capacity ?